ECU0:
- Receives:
- Fuel Level (10 bits) (from ECU3),
- Engine Coolant Temperature (10 bits) (from ECU4),
- Alive Signal (1 bit) (from ECU1).
- Sends:
- Light Sensor Value (10 bits),
- Doors (2 bits),
- Fuel Level Warning (1 bit),
- Engine Cooling Warning (1 bit),
- Alive Signal (1 bit),
- Error Message (1 bit) if ECU1 is not present.

ECU1:
Receives:
- Speed (10 bits) (from ECU4),
- Non-Driven Wheels Speed (10 bits) (from ECU2),
- Alive Signal (1 bit) (from ECU2).
Sends:
- RPM (10 bits),
- Gears (8 bits),
- ASR Warning (1 bit) if speed difference between the speed of the drive wheels and the speed of the non-driven is greater than 15 km/h,
- Alive Signal (1 bit),
- Error Message (1 bit) if ECU2 is not present.

ECU2:
Receives:
- Light Sensor Value (10 bits) (from ECU0),
- Alive Signal (1 bit) (from ECU3).
- Sends:
- Non-Driven Wheels Speed (10 bits),
- Light States (6 bits),
- Alive Signal (1 bit),
- Error Message (1 bit) if ECU3 is not present.

ECU3:
Receives:
- Speed (10 bits) (from ECU4) (M_ID = 0x502),
- Doors (2 bits) (from ECU0) (M_ID = 0x102),
- Alive Signal (1 bit) (from ECU4) (M_ID = 0x504).
- Sends:
- Fuel Level (10 bits) (M_ID = 0x401),
- Indicator Switch (3 bits) (M_ID = 0x402),
- Door Status (3 bits) (including Open Door Warning (1 bit)) (M_ID = 0x403),
- Alive Signal (1 bit) (M_ID = 0x404),
- Error Message (1 bit) if ECU4 is not present (M_ID = 0x405	).

ECU4:
Receives:
- Gears (8 bits) (from ECU1),
- RPM (10 bits) (from ECU1),
- Alive Signal (1 bit) (from ECU0).
Sends:
- Engine Coolant Temperature (10 bits),
- Headlight Switch (3 bits),
- Speed (10 bits),
- Alive Signal (1 bit),
- Error Message (1 bit) if ECU0 is not present.

Messages Received:
- Alive Signals (by ECU0 from ECU1) (by ECU1 from ECU2) (by ECU2 from ECU3) (by ECU3 from ECU4) (by ECU4 from ECU0)
- Fuel Level (by ECU0 from ECU3)
- Engine Coolant Temperature (by ECU0 from ECU4)
- Speed (by ECU1 from ECU4) (by ECU3 from ECU4)
- Non-Driven Wheels Speed (by ECU1 from ECU2)
- Light Sensor Value (by ECU2 from ECU0)
- Door Status (by ECU3 from ECU0)
- Gears (by ECU4 from ECU1)
- RPM (by ECU4 from ECU1)

Messages Sent:
- Alive Signals (by ALL ECUs)
- Error Messages if ECUs are not present (by ALL ECUs)
- Light Sensor Value (by ECU0)
- Door Statuses (by ECU0 and ECU3)
- Fuel Level Warning (by ECU0)
- Engine Cooling Warning (by ECU0)
- RPM (by ECU1)
- Gears (by ECU1)
- ASR Warning (by ECU1)
- Non-Driven Wheels Speed (by ECU2)
- Light States (by ECU2)
- Fuel Level (by ECU3)
- Indicator Switch (by ECU3)
- Open Door Warning (by ECU3)
- Engine Coolant Temperature (by ECU4)
- Headlight Switch (by ECU4)
- Speed (by ECU4)