ECU0:
- Receives:
- Fuel Level (10 bits) (from ECU3) (M_ID = 0x401),
- Engine Coolant Temperature (10 bits) (from ECU4) (M_ID = 0x501),
- Alive Signal (0 bits) (from ECU1) (M_ID = 0x204).
- Sends:
- Light Sensor Value (10 bits) (M_ID = 0x101) (200ms),
- Doors (2 bits) (M_ID = 0x102) (200ms),
- Fuel Level Warning (1 bit) (M_ID = 0x103) (400ms),
- Engine Cooling Warning (1 bit) (M_ID = 0x104) (400ms),
- Alive Signal (0 bits) (M_ID = 0x105) (200ms),
- Error Message (0bits) if ECU1 is not present (M_ID = 0x106) (200ms).

ECU1:
Receives:
- Speed (10 bits) (from ECU4) (M_ID = 0x502),
- Non-Driven Wheels Speed (10 bits) (from ECU2) (M_ID = 0x302),
- Alive Signal (0 bits) (from ECU2) (M_ID = 0x303).
Sends:
- RPM (10 bits) (M_ID = 0x201) (100ms),
- Gears (8 bits) (M_ID = 0x202) (200ms),
- ASR Warning (1 bit) if speed difference between the speed of the drive wheels and the speed of the non-driven is greater than 15 km/h (M_ID = 0x203) (400ms),
- Alive Signal (0 bits) (M_ID = 0x204) (200ms),
- Error Message (0 bits) if ECU2 is not present (M_ID = 0x205) (200ms).

ECU2:
Receives:
- Light Sensor Value (10 bits) (from ECU0) (M_ID = 0x101),
- Alive Signal (0 bits) (from ECU3) (M_ID = 0x404).
- Sends:
- Light States (6 bits) (M_ID = 0x301) (400ms),
- Non-Driven Wheels Speed (10 bits) (M_ID = 0x302) (100ms),
- Alive Signal (0 bits) (M_ID = 0x303) (200ms),
- Error Message (0 bits) if ECU3 is not present (M_ID = 0x304) (200ms).

ECU3:
Receives:
- Speed (10 bits) (from ECU4) (M_ID = 0x502),
- Doors (2 bits) (from ECU0) (M_ID = 0x102),
- Alive Signal (0 bits) (from ECU4) (M_ID = 0x504).
- Sends:
- Fuel Level (10 bits) (M_ID = 0x401) (200ms),
- Indicator Switch (3 bits) (M_ID = 0x402) (200ms),
- Door Status (3 bits) (including Open Door Warning (1 bit)) (M_ID = 0x403) (400ms),
- Alive Signal (0 bits) (M_ID = 0x404) (200ms),
- Error Message (0 bits) if ECU4 is not present (M_ID = 0x405) (200ms).

ECU4:
Receives:
- Gears (8 bits) (from ECU1) (M_ID = 0x202),
- RPM (10 bits) (from ECU1) (M_ID = 0x201),
- Alive Signal (0 bits) (from ECU0) (M_ID = 0x105).
Sends:
- Engine Coolant Temperature (10 bits) (M_ID = 0x501) (200ms),
- Speed (10 bits) (M_ID = 0x502) (100ms),
- Headlight Switch (3 bits) (M_ID = 0x503) (200ms),
- Alive Signal (0 bits) (M_ID = 0x504) (200ms),
- Error Message (0 bits) if ECU0 is not present (M_ID = 0x505) (200ms).

All Messages Received:
- Alive Signals (by ECU0 from ECU1) (by ECU1 from ECU2) (by ECU2 from ECU3) (by ECU3 from ECU4) (by ECU4 from ECU0)
- Fuel Level (by ECU0 from ECU3)
- Engine Coolant Temperature (by ECU0 from ECU4)
- Speed (by ECU1 from ECU4) (by ECU3 from ECU4)
- Non-Driven Wheels Speed (by ECU1 from ECU2)
- Light Sensor Value (by ECU2 from ECU0)
- Door Status (by ECU3 from ECU0)
- Gears (by ECU4 from ECU1)
- RPM (by ECU4 from ECU1)

All Messages Sent:
- Alive Signals (by ALL ECUs)
- Error Messages if ECUs are not present (by ALL ECUs)
- Light Sensor Value (by ECU0)
- Door Statuses (by ECU0 and ECU3)
- Fuel Level Warning (by ECU0)
- Engine Cooling Warning (by ECU0)
- RPM (by ECU1)
- Gears (by ECU1)
- ASR Warning (by ECU1)
- Non-Driven Wheels Speed (by ECU2)
- Light States (by ECU2)
- Fuel Level (by ECU3)
- Indicator Switch (by ECU3)
- Open Door Warning (by ECU3)
- Engine Coolant Temperature (by ECU4)
- Headlight Switch (by ECU4)
- Speed (by ECU4)